## Slide 1: Design and Application of Hybrid Classification System on Memory IC Testing
Ong Boon Ping
Tan Chin Gee
Han Dongchou Francis

## Slide 2: Description of Problem
In Memory IC testing, a number of electronic tests are conducted using the programmable automatic electronic tester.
Electronic testing is used not only to sort out chip failures, its results can also be used to find out the locations of failure inside the array. This will then help to identify the root cause of the failures.
A DRAM chip uses row and column to indicate the array cell position. Hence, it is important to understand whether the failures is coming from the row, column, or individual cell (or combination).

## Slide 3: Complications
Auto-test results can be affected by noise which can affect accuracy.
As part of yield enhancement, the focus is to probe for single bit (SB), row (ROW) and column (COL) failures inside the DRAM chips. The failures may happen as a combination.
Hence, it is hard to predict the nature of failures and currently, most of the verifications are done via manual inspection (after the IC is de-capsuled).

## Slide 4: Proposed Solution
A Data Set comprising IC testing data from 58 tests (58 features) and inspected failing mechanisms (8 classes, namely Overkill, SB, COL, SB+COL, ROW, SB+ROW, COL+ROW, SB+COL+ROW) has been gathered.
A Hybrid Classification Model is built with a capability to select the best solution presented by three techniques, namely Decision Tree, Multi-layer Perceptron and SVM.
The Competitive Agent in the model compares the accuracy, feature-to-class correlation and assigns penalty for severe mis-classification listed below:
  mis-classification as Overkill
  mis-classification into totally unrelated classes such as ROW as COL.

## Slide 5: Overall Design
The Hybrid Classification Model employs three techniques, namely the Decision Tree, MLP, and SVM.
The solutions from all techniques go through the Competitive Agent so that the optimal solution is selected.

## Slide 6: Data Set
The input data is in CSV format.
“1” represents test positive and “0” as test negative.
ID is dropped at the beginning.
“SB”,”ROW”,”COL” are inspection results. Other than these columns, the rest are automated test results.
Test and Train split are in ratio of 2:1.
The output classes are formed from the 3 columns from raw data, namely, SB, COL, ROW.

## Slide 7: Data Set
Expected class
#Forming 8 class from 3 columns, coded as 0 to 7
#['Overkill','SB','COL','SB+COL','ROW','ROW+SB','ROW+COL','SB+ROW+COL’]
y = test_data.SB+2*test_data.COL+4*test_data.ROW

## Slide 8: Decision Tree
Analysis:
For DT, we are using the DecisionTreeClassifier to perform multi classification on the data set.
Two parameters are tuned for optimal performance – Best Depth and Best Impurity Decrease. See codes on the right.
Fine tuning is then done again on impurity decrease and min_weight_fraction_leaf based on accuracy.
The model is then passed to the Competitive agent.
for DEPTH in range(20,40,1):
dt = DecisionTreeClassifier(criterion='entropy’, max_depth=DEPTH,random_state=0, min_impurity_decrease=0.0001,min_weight_fraction_leaf=0.001)
dt.fit(X_train, y_train)
#post_pruning
prune_duplicate_leaves(dt)
print(DEPTH,dt.score(X_test, y_test))
if dt.score(X_test, y_test)>max_accuracy:
max_accuracy=dt.score(X_test, y_test)
best_depth=DEPTH
#prints for tuning the DEPTH - Best DEPTH = 29
print("DEPTH = ", DEPTH)
Code for finding the Best Depth:
Code for finding the Best Impurity Decrease:
for impurity_decrease in range(5,20,1):
dt = DecisionTreeClassifier(criterion='entropy',max_depth=best_depth, random_state=0,min_impurity_decrease=impurity_decrease*0.00001, min_weight_fraction_leaf=0.001)
dt.fit(X_train, y_train)
#post_pruning
prune_duplicate_leaves(dt)
print(best_depth,impurity_decrease,dt.score(X_test, y_test))
if dt.score(X_test, y_test)>max_accuracy:
max_accuracy=dt.score(X_test, y_test)
best_impurity_decrease=impurity_decrease*0.00001

## Slide 9: MLP
For MLP, we have two parameters to tune – Learning Rate and Momentum.
For optimum results, the initial Learning Rate was set to 0.001 and the Momentum to 0.995.
scaler = StandardScaler()
scaler.fit(X_train)
X_test1=X_test
X_test2=X_test
X_train = scaler.transform(X_train)
X_test1 = scaler.transform(X_test1)
from sklearn.neural_network import MLPClassifier
mlp = MLPClassifier(hidden_layer_sizes=(10,), learning_rate='constant', learning_rate_init=0.001, max_iter=1000, momentum=0.995, verbose=2)
mlp.fit(X_train, y_train)
predictions = mlp.predict(X_test1)
print("Accuracy", metrics.accuracy_score(y_test, predictions))
print(multilabel_confusion_matrix(y_test,predictions))
print(classification_report(y_test,predictions))
print(mlp.coefs_[0][1])
The program:
Analysis:

## Slide 10: SVM
For SVM, we are using the Radial Basis Function (RBF) kernel. Two parameters have some levels of effect on the results, and they are the gamma and C.
The gamma parameter defines how far the influence of a single training example reaches, with low values meaning ‘far’ and high values meaning ‘close’. The gamma can be seen as the inverse of the radius of influence of samples selected by the model as support vectors.
The C parameter trades off correct classification of training examples against maximization of the decision function’s margin. Larger values of C means that a smaller margin will be accepted. A lower C gives a larger margin. This would mean a simpler decision function, but it erodes training accuracy. Hence C is like a regularization parameter in the SVM.
In the program, it is established the optimal C is 4.
It is found that gamma doesn’t have much effect, and it is left at 5.
from sklearn.svm import SVC
from sklearn.multiclass import OneVsRestClassifier
for C_val in range(1,10,1):
svm=OneVsRestClassifier( SVC(kernel="rbf", gamma='auto_deprecated', C=C_val) )
svm.fit(X_train, y_train)
predictions = svm.predict(X_test1)
svm_pred=predictions
from sklearn.metrics import classification_report, confusion_matrix
print("C= ", C_val)
print(multilabel_confusion_matrix(y_test,predictions))
print(classification_report(y_test,predictions))
print("Accuracy on training set: {:.3f}".format(svm.score(X_train, y_train)))
print("Accuracy on test set: {:.3f}".format(svm.score(X_test1, y_test)))
print("============================================")
#optimal C = 4
The program:
Analysis:

## Slide 11: Competitive agent
The Competitive Agent gives a score to each technique, namely, Decision Tree, MLP, SVM based on feature correlation and accuracy.
Penalty is given to each model based on mis-classification type as illustrated by the Confusion Matrix.

## Slide 12: Feature Correlation
For each of the 58 tests (features), the model will compute the Expected Failing Mode and Simulated Failing Mode.
“Expected Failing Mode” is computed based on X_test entries with targeted feature set to 1. In each entry, the Entry Significance will be
calculated as . This is because the more unique
the testing result, the greater the significance of the entry.

## Slide 13: Feature Correlation
The total of all Entry Significance will be the sum of weightage.
For each failing mode such as SB, ROW and COL, the entry significant will be multiply by SB/ROW/COL data on entry. If failing mode significance is more than 50% of the total, then the feature is expected to be significantly related to the failing mode.
(note: failing mode value can be 1 or 0 and hence must be smaller or equal to total)

## Slide 14: Feature Correlation
For each technique, namely DT, MLP, SVM, the most related class to the feature is also found in a similar formula but based on the predicted outcome of each entries.
If the model prediction is matching the expectation, it gets a score. Otherwise n score is given.
The score given to each feature will be

## Slide 15: Feature Correlation
Example:
In a test dataset of 1000 entries, feature A is 1 in 100 entries.
In the 1st entry, Features A,B and C are set to 1, 0, 0. Hence, significance is 1/3=0.33.
SB is 1 but COL and ROW are 0. Hence SB significance is 0.33 but B,C is 0.
At the 2nd Entry, Features A,D are set to 1, 0. Significance is ½=0.5 . Total significance is 0.33+0.5=0.83
SB and COL is 1 but ROW are 0. Hence SB total significance is 0.83 but B is 0.5 and C is still 0.

## Slide 16: Feature Correlation
After accounting for all the 100 entries, total significance is 50 while SB is 36, COL is 9, ROW is 1. Hence, we expect SB to be most related to the feature A.
Using model prediction outcome on the same 100 entries, we found that MLP and SVM chose SB for feature A but DT chose COL.
Hence, DT gets 0 score for feature A. MLP and SVM gets a score of 100/1000 = 0.1.

## Slide 17: Accuracy
The accuracy of each model will also be added on top of Feature Correlation Score.

## Slide 18: Mis-classification penalty
In this scenario, not all mis-classification are subjected to penalty.
Cases such as ROW classified as related ROW+SB will be ignored.
Mis-classification as Overkill for valid failing mode or mis-classification as other non-related failing mode will be penalized.
Penalty points are calculated as
Penalized score will be deducted from total score.

## Slide 19: Best Solution
The Competitive Agent will choose the technique with best Total Score. The detail related to the chosen technique will be displayed.
The Total Score= Feature Correlation Score + Accuracy Score – Mis-Classification Penalty